## Slide 1
Chapter 3
Shear

## Slide 2
Example 1: Sheared workpiece
the shearing of the piece results in the sliding of the straight section S1 against the straight section S2 which is in direct contact with it.
Blade 1
Blade 2

## Slide 3
1.Definition:
A beam is subjected to pure shear stress when the cohesive torsor at the centre of gravity of a section has the form
𝜏𝑐𝑜ℎ =
0 | 0
𝑇𝑦 | 0
𝑇𝑧 | 0

## Slide 4
1.Definition :
Shear stress occurs when a beam is subjected to two equal and directly opposed forces whose support is in a plane perpendicular to the mean line.

## Slide 5
1.Definition :
Under the action of these two forces, the beam tends to separate into two parts sliding relative to each other in the plane of the straight section (Σ)

## Slide 6
The only internal force is T (N = Mf = 0).According to the equilibrium T=F.
2.Shear force T

## Slide 7
Each surface element 𝒅𝑺 supports a shear stress 𝝉 contained in the sheared section 𝑺 .
3.State of constraint

## Slide 8
Example 2
Three identical blocks of wood (1), (2) and (3) are glued together. The assembly supports a load F along its axis of symmetry. The glued surfaces are ABCD and A'B'C'D'.
glued surfaces

## Slide 9
To calculate T, we isolate block (1) and study its equilibrium.
Note
A simple relationship can be deduced between the applied force F and T :
Where n is the number of sheared surfaces.

## Slide 10
4.Shear stress τ
In shear, normal stresses are null. It is supposed that all tangential stresses are the same. In other words, there is a uniform stress distribution in the sheared section.

## Slide 11
Example 2
Take example 2 with F=200 daN, AB=CD=3 cm, AD=BC=10 cm. Calculate τ in the glued joint.

## Slide 12: Solution

## Slide 13
5.Resistance condition
Rps: practical resistance to sliding or shearing (permissible stress). Res: elastic limit in shear. s: safety coefficient.
Example 3 Let's return to example 2.
If the admissible stress in the glued joint is 900 kPa, determine the maximum load F that can be supported
(Admissible stress)

## Slide 14: Solution

## Slide 15
6. Deformation - Sliding angle γ
Rigid plate
Elestometer block
gluing
Deformation can be characterized by the angle γ, known as the angle of sliding angle.
if γ is small

## Slide 16
7.Relation between τ and γ
As in the case of tension, in the elastic domain, the relationship between τ and γ is linear.
τ = G.γ
γ: sliding angle (radian)
G: transverse modulus of elasticity (MPa)
Where 𝜈 is the Poisson coefficient
Coulomb Modulus G

## Slide 17
Example 4
Let's take the example of the elastomer block (c × b × h) with c=50mm, b=100 mm and G=800 kPa. Determine γ if T=100 daN and h=25 mm. calculate a.

## Slide 18
Solution

## Slide 19
Example 5
F=10000 daN, the axes are made from the same steel with an admissible shear stress of 5 daN/mm2.

## Slide 20
one sheared section
Two sheared section

## Slide 21
Example 6
For the above connection with three steel bolts, d= 12mm, the permissible shear stress is Rps = 30 daN/mm2
Determining the admissible force

## Slide 22
20358