## Slide 1: Introduction to Medical Imaging
KHEMIS Kamila

## Slide 2
Medical imaging is a discipline within the medical field which involves the use of technology to take images of the inside of the human body.
These images are used in diagnostics, as teaching tools, and in routine healthcare for a variety of conditions.
Medical imaging is sometimes referred to as diagnostic imaging, because it is frequently used to help doctors arrive at a diagnosis, and there are a number of different types of technology used in medical imaging.
The goal of medical imaging is to provide a picture of the inside of the body in a way which is as non-invasive as possible.
An imaging study can be used to identify unusual things inside the body, such as broken bones, tumors, leaking blood vessels, and so forth. One of the most famous types of diagnostic imaging is the x-ray, which uses radiation to take a static image of a specific area of the body.
Definition

## Slide 3
Measurement and recording techniques which are not primarily designed to produce images, such as electroencephalography (EEG), magneto encephalography (MEG), electrocardiography (ECG) and others, but which produce data susceptible to be represented as maps (i.e. containing positional information), can be seen as forms of medical imaging.
Résumé
L’imagerie médicale est l’utilisation de la technologie pour obtenir une image de l’intérieur du cops humain d’une manière la moins invasive possible et généralement dans un le but de diagnostiquer une pathologie, mais aussi parfois pour guider un geste thérapeutique

## Slide 4
L’imagerie médicale concerne le coté technologique autrement dit les dispositifs d’imagerie médicale.
Image
A quoi ressemble une image ?
Celles qu’on a l’habitude de voir :
Pas besoin d’interprétation

## Slide 5
A quoi ressemble une image du domaine médical ?
Exemple 1 : Dermatologie
Le dispositif : Dermascope
L’image

## Slide 6
A quoi ressemble une image du domaine médical ?
Exemple 2 : Endoscopie
Le dispositif : Cologne endoscopique
L’image

## Slide 7
Autres images du domaine médical : exemple 3
Le dispositif : scanner
L’image
Cela ressemble de moins en moins des images qu’on connait
Besoin d’interprétation

## Slide 8
Le dispositif : Imagerie par résonnance magnétique
(IRM)
L’image
Autres images du domaine médical : exemple 4

## Slide 9
Le dispositif : Echographe
L’image
Autres images du domaine médical : exemple 5

## Slide 10
Comment obtient-on ces différentes images ?
Commençons par l’image du domaine de l’optique (images de notre quotidien, mais également dermatologie, endoscopie
Source de lumière (excitation)
Interaction de la lumière avec la scène (phénomène de réflexion)
Capture des rayons réfléchis (la caméra, l’oeil)

## Slide 11
Vision diurne ( cones)/ nocturne (batonnets)
Domaine de l’opto-éléctronique

## Slide 12
Le résultat : image analogique / image numérique
Pixel : picture element
On entre dans le domaine du traitement et de l’analyse d’image

## Slide 13
Qu’en est-il pour les autres exemples du domaine médical ?
Source d’excitation : Rayons X, champs magnétique , ultrasons
Le même principe mais :
Interaction de la source d’exitation avec les tissus humains
phénomènes de réflexion
phénomènes d’absorption
Réaction nucléaire…
Acquisition du signal
1
2
3
Le résultat : l’image numérique  juxtaposition de pixels

## Slide 14
Evolution of Medical Imaging
Medical imaging began with the discovery of X- Rays by Wilhelm Conrad Röntgen in 1895 and his work showing that these rays could be used to peer inside the body and visualize bony structures.
From this Nobel Prize winning discovery to the modern day, there are now many means by which the internal structures of the body can be assessed without the need for cutting it open (non-invasive).
first medical x ray by wilhelm Rotgen of his wife anna bertha ludwig’s hand 18951222
fr.wikipedia.org

## Slide 15
Medical Imaging Techniques
Medical Radiography
Computed Tomography (CT)
Ultrasound Imaging
Positron Emission Tomography and Single Photon Emission Tomography
Magnetic Resonance Imaging (MRI)
X ray
US
Radioactif Nuclei
Magnetic field

## Slide 16
Medical Radiography
Medical radiography is a broad term that covers several types of studies that require the visualization of the internal parts of the body using x-ray techniques.
During a radiographic procedure, an x-ray beam is passed through the body.
A portion of the x-rays are absorbed or scattered by the internal structure and the remaining x-ray pattern is transmitted to a detector so that an image may be recorded for later evaluation.
The recoding of the pattern may occur on film or through electronic means
Medical Radiography is considered a noninvasive procedure, which means that the process of acquiring a medical image does not penetrate the skin.

## Slide 17
Projetional Radiography (principle and examples)

## Slide 18
Computed Tomography (CT)
Computed Tomography (CT) is a noninvasive medical imaging procedure that uses a combination of X-rays and computer technology to produce detailed images of the inside of the body.
The procedure involves rotating a narrow beam of X-rays around the patient's body, producing signals that are processed by the machine's computer to generate cross-sectional images, or "slices."
These slices are called tomographic images and can give a clinician more detailed information than conventional X-rays.
CT scans are often done with or without contrast agent to improve the radiologist's ability to find any abnormalities.
CT scans can be performed on every region of the body for a variety of reasons, including diagnostic, treatment planning.

## Slide 19
Principle of the CT Scan
The term « computed tomography », or CT , refers to a computerized x-ray imaging procedure in which a narrow beam of x-rays is aimed at a patient and quickly rorated around the body, producing signals that are processed by computer to generate cross-sectional images or slices of the body.
These slices are called tomographic images.
Successive slices can be computed to produce a three dimentional image of the patient allowing easier identification and location of basic structures as well as possible tumors or abnormalities

## Slide 21
Computed Tomography (CT)
The personnel that perform CT scans are called radiographers or radiology technologists

## Slide 22
Echography :
Imaging technique based on the emission and reception of mechanical sound waves
Ultrasonography, also known as sonography, is a non-invasive imaging test that uses high-frequency sound waves to produce images of organs, tissues, and other structures inside the body.1 The test uses a transducer that converts electrical current into sound waves (with a frequency greater than the hearing frequency range of the human ear (i.e., 20 kilohertz (kHz)) by piezoelectric crystals located inside the transducer or probe)
The such produced waves, are sent into the body's tissues.
The sound waves bounce off structures in the body and are reflected back to the transducer, which converts the waves into electrical signals.
Ultrasonography images may be called sonograms.
Endoscopic ultrasonography involves attaching the transducer to an endoscope and passing it into the body.
Transesophageal echocardiography involves passing the endoscope down the throat to view the heart.

## Slide 23
Ultrasound imaging, or ultrasonography (US), uses high-frequency sound pulses that are emitted from a hand-held ultrasound transducer, or probe.
  The transducer is applied to the patient's skin via a coupling gel, and the sound pulses are reflected back to the transducer from structures within the patient.
  The magnitude of the reflected sound, or “echo,” is converted into a gray-scale image.
  Tissues that are highly reflective of the sound, or “echogenic,” such as bone, appear bright. Tissues that allow transmission of the sound pulses, or are poorly echogenic, such as fluid, appear dark or black.
  Substances that are moving, such as flowing blood, can be evaluated using a technique known as Doppler imaging, which demonstrates the direction and velocity of movement.
  Images are acquired and viewed in real time and are therefore amenable to image-guided procedures such as biopsy, injection, and aspiration.
  US does not use ionizing radiation and is therefore safe to use during pregnancy and in the pediatric population.

## Slide 24
hand-held ultrasound transducer (probe)
2D echography
3D echography

## Slide 25
Echocardiography, also known as cardiac ultrasound, is a medical imaging technique that uses high-frequency sound waves to create pictures of the heart's valves and chambers.
It is used to diagnose and manage heart disease.
There are different types of echocardiograms, including standard ultrasound and Doppler ultrasound. The visual image formed using this technique is called an echocardiogram or cardiac echo

## Slide 26
PET or SPECT are two imaging modalities relative to a field of medecine called nuclear medecine
Both techniques uses a radioactive tracer that is swallowed, inhaled or injected into a vein of the patient befor the examination.
Certain organs and tissues then absorb the tracer.
The tracer emits gamma rays that are detected by PET or Gamma camera.
The amount of gamma rays is proportional to the omount of radioactif tracer which represent the working of tissues or organ (functional image)
Radioisotope based imaging systems

## Slide 27
Positron Emission Tomography device
PET principle

## Slide 28
Single Photon Emission Tomography device (Gamma Camera)

## Slide 29
PET (positron emission tomography) scan of the brain

## Slide 30
Notes: https://www.youtube.com/watch?v=yrTy03O0gWw

## Slide 31
Magnetic Resonance Imaging (MRI)
Magnetic Resonance Imaging (MRI) is a non-invasive medical imaging procedure that uses a strong magnetic field, magnetic field gradients and radio waves to produce detailed images of almost every internal structure in the human body, including organs, bones, muscles, and blood vessels.
It is especially helpful to collect pictures of soft tissue such as organs and muscles that don't show up on x-ray examinations.
It is based on sophisticated technology that excites and detects the change in the direction of the rotational axis of protons found in the water that makes up living tissues.
MRI is often used for disease detection, diagnosis, and treatment monitoring

## Slide 32
MRI device
MRI images

## Slide 34
Notes: https://www.youtube.com/watch?v=djAxjtN_7VE

## Slide 36
Imaging Technique | Imaging Type | Source | Ionizing Radiation
Echography | Reflection | Utra sounds | No
Radigraphy/CT scan imaging | Transmition | X ray | Yes
MRI | emission | Magnetic Field + Radio Frequence | No
Radioisotope imaging | emission | Gamma photons | Yes

## Slide 37: Summarizing
Medical imaging refers to the visualization of body parts, tissues, or organs for use in clinical diagnosis, treatment, and disease monitoring.
It encompasses the fields of radiology, nuclear medicine, optical imaging, and image-guided intervention.
Radiology is a branch of medicine that deals with radiant energy in the diagnosis and treatment of diseases by using imaging technologies.
There are several important medical imaging technologies, including X-ray, ultrasound, computed tomography (CT), magnetic resonance imaging (MRI), positron emission tomography (PET), and biophotonics.
X-ray is the most common form of medical imaging, which is high-energy radiation that can easily penetrate materials such as skin and tissues but cannot easily penetrate metals and bone.