## Slide 1: control system and regularization
BE521 _ L3
Produced by:
Mme Iles Amel
بسم الله الرحمن الرحيم

## Slide 2: Overview of lecture
Lecture1: Introduction to control systems and regularization
Lecture 2: Transfer function of control system
Lecture 3: Time response analysis
Lecture 4: Frequency response analysis
Lecture 5: Stability
Lecture 6: Accuracy
Lecture 7: Correctors

## Slide 3: Lecture 1
Introduction to control systems

## Slide 4
A system is said to be ‘control’ when it performs a specific task without requiring human intervention.
A control system consists of subsystems or processes (or plants) assembled for the purpose of controlling the output of the processes.
Exemples :
1. An air conditioner maintaining the temperature of the room
2. A car moving from rest to a speed of 100 km/hr
3. Circuit with V input and current output
Control System
Input, stimulus
Output, response
Actual response
Desired response
Introduction

## Slide 5
Exemple : A man driving a car
when driving a car, we often seek to ensure:
A speed: Action of the feet on the pedal.
A determined direction: Action of the arms on the steering wheel.
This system ‘car’ has quantities on which we act to adjust other quantities :
The first quantities are called ‘input quantities’,
the others are called ‘output quantities’.

## Slide 6
In this exemple:
The control system : is the car
input quantities :
  Pedal position
  Angular position of the steering wheel
output quantities :
  car speed
  Orientation
  Other quantities can act on the system :
  parasitic quantities : such as wind, fog (brouillard) or any kind of road conditions,

## Slide 7: Block diagram of control system
Block diagram : is a graphical representation of a control system.
1. Open loop system
An open loop control system is a system in which the control action is totally independent of output of the system .
The accuracy of the system depends on the experience of user.
Exemple:
Immersion water heater (immerger l’eau chaud): No feedback mechnism to tell how hot it is.
process
Reference Input
Output
Control
Control System

## Slide 8
In the closed loop system, the output is meaasured continuously and is fed back to the input.
The presence of feedback improves the accuracy of the system.
Process
Controller
feedback
Reference Input
Output,
Error detection
2. closed loop system

## Slide 9
In the car exemple:
The control system : is the car
Input : what I want to get, example : I want to get a speed of 100Km/h
Disturbances: these are phenomena that can modify the stability of a regulation loop.
Feedback element : correspond to the sensor ; it is a measuring device, here it corresponds to the speed dial, it is necessary to measure the speed. Also the human vision needed to change the direction of the vehicle at any time.
Onput : this is what I actually have, example I have a speed of 80 km/h.
Comparator: Permanently compares the input and the output variable and gives the result of this comparison to the corrector.
Error ε: it is the calculated error between the input and output signals.
Corrector : represented by the human in this example, this organ corrects the error ε.

## Slide 10: AUTOMATIC regularization : How to characterize the performance of a regulated system?
A regulated system is characterized by :
    • its accuracy;
    • its speed ;
    • its stability

## Slide 11: accuracy of the system
the ability of the system to get as close as possible to the setpoint (point de consigne).
1 : input command
2 : imprecise system.
3 : accuracy of the system at stady state.
E2 : static error related to curve 2. E3 : static error related to curve 3.
The error is expressed as a percentage of the setpoint value

## Slide 12: Speed :
It is the ability of the system to reach its stable regime as soon as possible. The speed of a system is defined by its response time tr (the smaller tr, the faster the system is said to be).

## Slide 13: stability :
For a constant setpoint the output must tend towards a stable response. There are 3 types of responses: stable; oscillating and unstable
Oscillant system
Unstable system
Stable system
Curve 1 : Input
Curve 2 : Output of the system

## Slide 14: Remark
    With a time signal, we can characterize the accuracy; system speed and stability.
    With a frequency signal, we can find the stability, the filtering, the bandwidth and the phase shift caused by the system.

## Slide 15: Control SYSTEMS
The systems can be classified into 2 categories :
Static systems : instantaneous response ; the time variable does not influence the system operation.
Example: resistor
Resistor (R)
i(t)
u(t)
Dynamical systems : these systems have a response that depends on both present excitation and past responses
Example: Capacitor C
During a time interval, the electric charge q(t) accumulated in this capacitor is:
q(t) =q(0)+c.u(t)
Where q(0) is the load at the initial time t=0.
Dynamical systems can be continuous; their functioning evolves continuously over time.
Continuous time systems are modeled by a differential equation relating the input and the output of the system.

## Slide 16: LINEAR and time invariance (LTI) SYSTEMS
Additivity (superposition) : the system obeys the additivity property if, to the sum of the excitations r1(t) and r2(t), the system makes correspond an output quantity y(t) which is the sum of the two output quantities y1(t ) and y2(t).
LTI
System
y1(t)
r1(t)
LTI
System
y2(t)
r2(t)
LTI
System
y1(t)+y2(t)
r1(t)+r2(t)
A linear system is a system that obeys the properties of additivity and homogeneity.

## Slide 17
Homogeneity: the system obeys the homogeneity property if, to an excitation 'a.r(t): with ‘a’ a real coefficient', the system matches another output quantity which is the output quantity y(t) multiplied by the same factor a: a.y(t).
LTI
System
y(t)
r(t)
a.r(t)
a.y(t)
r(t)
1
2
1
2

## Slide 18
What time is it?
Time invariance
LTI
System
y(t-a)
r(t-a)