## Slide 1
control system and regularization
BE521 _ L3
Produced by:
Mme Iles Amel
بسم الله الرحمن الرحيم

## Slide 2
Transfer function of contol system
Lecture 2

## Slide 3: laplace Transform
Laplace Transform (LT) is the tool to represent the frequency domain of a time domain fonction.:
F(p) : Laplace Transform F(p) = L [f(t)]
P=σ+jω
Laplace Transform is defined for t>0 ;
f(t)=0 when t<0.
Inverse Laplace Transform
Note: Laplace Transforms convert differential equations into algebraic equations. They are related to frequency response

## Slide 4
Laplace Transform property
For a continuous time signal f(t), we define its Laplace transform by the signal F(p) where p is the Laplace variable,
Linearity:
The Laplace transform is a linear transformation:
if f(t) = a f1(t) + b f2(t) F(p) = aF1(p) + bF2(p)
derivative :
if L [f(t)] = F(p) L [df(t)/dt] = F’(p)
F’(p) = pF(p)-f(0)
F’’(p) = F(p)-pf(0)-f’(0)
Multiple derivative : derivative to the Power of n
(p)= L [ f(t) / d ]
(p) = F(p) - f(0) - f’(0) -…………….. - (0)

## Slide 5
Convolution property :
L[f1(t) f2(t)]= F1(p) . F2(p)]
Convolution in time domain is the multiplication in frequency domain.
Time shifting:
L [f(t-ζ)]=F(p)
final value : Value of a function at t=∞. (steady state value)
Initial value : Value of a function at t=0; p tends towards infinity.
frequency shifting:
L [f(t)]=F(p+ζ)

## Slide 6
Signals applied to the inputs
Unit Impulse signal : Dirac Delta :
δt=∞
If the input is an impulse signal, the response is an impulse response
G(p)
S(p)
E(p)
The Laplace Transform of the Dirac Impulse is :
TL(δ(t))=1
S(p)=G(p).E(p)
E(p)=1
S(p)=G(p)

## Slide 7
2. Step Input :
If the input is a step signal, the response is a step response
G(p)
S(p)
E(p)
The Laplace Transform of the step input is :
TL(e(t))= E(p)=
S(p)=G(p).E(p)
If we have an unit step input : a=1
S(p)=G(p)/p
Signals applied to the inputs

## Slide 8
3. Ramp Input :
G(p)
S(p)
E(p)
The Laplace Transform of the ramp input is :
TL(e(t))= E(p)=
S(p)=G(p).E(p)
If we have an unit ramp input a=1
S(p)=G(p)/
Signals applied to the inputs

## Slide 9: Introduction
To understand and control complex systems, one must obtain mathematical models of these systems.
It is the pictorial representation of the cause-and-response relationship between input and output of a physical system.
Control System
Output s(t)
Input e(t)

## Slide 10
System h(t)
Output s(t)
Input e(t)
By Convolution property
S(p)=E(p). H(p)
Time domain
S(t)=e(t)*h(t)
S(t)=
frequency domain
Mathematical Modeling of Physical Systems:
A mathematical model is a set of equations that represents the dynamics of the system accurately.
Because the systems under consideration are dynamic in nature, the mathematical equations are usually differential equations.

## Slide 11
If m ≤ n, the rational function is called proper. If m < n, it is strictly proper.
where :
ai and bi are constant coefficients
s(t) output signal
e(t) input signal
Differential equations of n order :
Mathematical Modeling of Physical Systems
Differential Equations:
The dynamics of many systems, whether they are mechanical, electrical, thermal, economic, biological, and so on, may be described in terms of differential equations:

## Slide 12
Système
E(t)
S(t)
where the coefficients ai and bi are constant real numbers. Then the polynomial has n complex roots. Furthermore, if all coefficients are real, then all non-real roots of f(x) appear in complex conjugate pairs.

## Slide 13
Transfer Function :
  Transfer function is the ratio of Laplace Transform of output to the Laplace Transform of input, when all the initial conditions are assumed to be zero.
System
H(p)
E(p)
S(p)
Transfer fonction of this system :
S(t)=e(t)*h(t)
By Convolution property
S(p)=E(p). H(p)
By use of Laplace transform we can convert common functions of time t into algebraic functions of complex variable s:
The Laplace Transform:
The transfert fonction H(p) of n order system :
H
If m ≤ n, the rational function is called proper

## Slide 14: Example : electric System
From the circuit, the output voltage, vs(t) is equal to the voltage across capacitor, vc(t).
(t)
Apply Kirchhoff's Voltage Law (KVL) around the loop
Loop IJKL :
Loop KLMN :
Consider the following series of the RLC circuit. It is having an input voltage, Ve(t) and the current flowing through the circuit is i(t).

## Slide 15
  Apply the Laplace Transform: all the initial conditions are assumed to be zero.
(t)
(p)
L[(t)]
(t)
(p)
L[(t)]
(t)
(p)
L[(t)]
TL
p(p)
TL
(p) (p)
We have :
=Cp
Remplacing I(p) in the equation:

## Slide 16: The transfer fonction h(p)
(p) =(1+R.C.p+L.C. )
This equation has the form of 2nd Order System :
Where k = 1 static gain , = : damping ratio and = undamped natural frequency

## Slide 17: The Partial Fraction Decomposition

## Slide 18: The Partial Fraction Expansion
ai and bi are real coefficients
polynome have n roots ‘reals or complexs’: -,…, -
      Simples roots:
are the residue :
= with i=1,2,….,n
By calculating the Laplace inverse transform, the temporel response y(t) is given by :
y(t)= u(t)
u(t) is the input of the système
If we can find coefficients Ci such that
then this is the PARTIAL FRACTION EXPANSION of G(p)
We first separate G into parts:

## Slide 19
      Real, Repeated Roots:
Sometimes G has a repeated pole:
The Partial Fraction Expansion:
= avec j=1,2,….,n
The inverse Laplace transform :
y(t)= u(t)
In this case, we CAN NOT use simple expansion . Instead we have
Residues are:

## Slide 20
Series Connection:
In this case, the output of one system feeds directly into the input of another system.
G1(p)
E(p)
S1(p)
G2(p)
S2(p)
Gn(p)
Sn (p)
S(p)
S(p)
G(p)
E(p)
Block Diagram Manipulation

## Slide 21
Parallel Connection:
In this case, two (or more systems) obtain the same input U(s), and their outputs are summed together to produce the output of the overall system.
G1(p)
G2(p)
Gn(p)
E(p)
S(p)
+
S(p)
G(p)
E(p)

## Slide 22: Transfer Function of a closed loop system (cLTF) (with negative feedback)
e
E(p)
S(p)
G(p)
-
+
H(p)
S(p)
(p)
E(p)
R (p)
S (p) = E (p) - R (p))G (p)
S (p) = (E (p) - S (p) H (p)) G (p)
S (p) = E (p) G (p) - S (p) H (p) G (p)
S (p) (1+ H (p) G (p)) = E (p) G (p)
closed loop transfer function

## Slide 23
Unit Feedback Connection.
e
E(p)
S(p)
G(p)
-
+

## Slide 24: open loop transfer function (OLTF)
A partir de la Boucle Fermée (BF), on « déconnecte » le retour !
e
E(p)
S(p)
G(p)
-
+
H(p)
S1(p)
Association de deux comparateurs :
E(p)
S(p)
-
+
X(p)
-
+
Y(p)
S(p)=E(p)-X(p)-Y(p)

## Slide 25
A gauche d’un élément :
Déplacement de comparateurs :
G(p)
E(p)
S(p)=E(p)G(p)-X(p)
-
+
X(p)
G(p)
E(p)
S(p)=(E(p) -X(p)/G(p))G(p)
=E(p)G(p)-X(p)
-
+
X(p)
1/G(p)

## Slide 26
A droite d’un élément :
Déplacement de comparateurs :
G(p)
E(p)
S(p)=(E(p)-X(p)) G(p)
-
+
X(p)
G(p)
E(p)
S(p)=E(p)G(p)-X(p) G(p)
=(E(p)-X(p)) G(p)
-
+
X(p)
G(p)

## Slide 27: problems
Example 1. Find the Laplace Transform of f(t) = ; t 0, where a R.
Solution:
Example 2. Find the Laplace Transform of the unit step function 1(t), defined as
TL(1(t))=

## Slide 28
Exemple 3.

## Slide 29: problems
Exercice 1: Find system transfer function between voltage drop across the capacitance and input voltage in the followingRC circuit.
Solution:

## Slide 30: problems
Exercice 2: Obtain the pole-zero map of the following transfer function.
G
Solution:

## Slide 31: problems
Exercice 2: Expand the following equation of Laplace transform in terms of its partial fractions and obtain its time-domain response.
Y
Solution:
The following equation in Laplacetransform is expandedwith its partial fractions as follows.
Taking Laplace inverse of above equation,
y(t) = -2 + 4

## Slide 32: problems
Example1: Let us reduce the following block diagram to canonical form.

## Slide 33
ε(p)=E(p)+Sretour​(p)
Si l'entrée est positive et le retour est positif (+) : C'est une rétroaction positive (ou contre-réaction positive).
  La formule est : F=G/(1−GH)​
  C'est la formule qui rend votre correction correcte.
La rétroaction positive est rarement utilisée pour l'asservissement (régulation), car elle a tendance à rendre le système instable. L'ajout d'un retour positif amplifie l'erreur au lieu de la corriger.
le bloc qui calcule l'erreur (E−R) est souvent appelé comparateur parce qu'il compare la consigne et la mesure, mais sur un schéma bloc, c'est un sommateur dont l'une des entrées est affectée du signe négatif (− ).

## Slide 34: Exemple 2
Consider the block diagram shown in the following figure. Let us simplify (reduce) this block diagram using the block diagram reduction rules.

## Slide 39: Exemple 3
Determine the transfer function Y(s)/R(s).