## Slide 1
control system and regularization
BE521 _ L3
Produced by:
Mme Iles Amel
بسم الله الرحمن الرحيم

## Slide 2: lecture 3
Time response analysis

## Slide 4: Introduction :
The time response consists of two parts.
Transient response: The response of a system from rest or equilibrium to settle down (se stabilise) at steady state.
Steady state response: The part of time
response that remains (maintient) after transient response

## Slide 5: Introduction :

## Slide 6: Introduction :
‘pôles’ : The complex numbers −p1, −p2, . . . , −pn are the roots of D(s) and are called the poles of F(p).
‘zeros’: The complex numbers −z1, −z2, . . . , −zm are the roots of N(s) and are called the zeros.
Control system(n)
s(t)
e(t)
Zeros and Poles

## Slide 7
In general, the performance of a control system is characterized by the following three criteria:
Precision: It is defined by two parameters: static error and dynamic error.
Speed/Bandwidth: Speed is determined by the response time.
Damping/Stability: Good damping is the ability of an oscillating system to be sufficiently damped and not exhibit significant overshoot.
An ideal control system is, therefore, fast, precise, and stable.
Time Response of Physical Systems:

## Slide 8
Time Response of Physical Systems:
It measures the response (output) of the physical system in time-domain when subjected to one of the standard test signals as an (input).

## Slide 9: Time Response of 1st Order Systems:
τ: Time constant, sec ,
s(t) is response of the system and
e(t) is input excitation
Consider the following block diagram of the closed loop control system. Here, an open loop transfer function, 1/sT is connected with a unity negative feedback.
s(t)
e(t)
+
-
=
=
=K/TP
Pole-zero map of a first-order system

## Slide 10: Time Response of 1st Order Systems:
A Governing differential equation is given by
L [e(t)] =E(p)
L [s(t)] =S(p)
By assuming zero initial Conditions:
L [ds(t)/dt] =pS(p)
Transfer fonction of 1st order system :
Where T: Time constant
s(t)+τ Ke(t)
Where, τ: Time constant, sec ,
K: Static sensitivity (units depend on the input and output variables) ,
s(t) is response of the system and
e(t) is input excitation
The System transfer function is

## Slide 11
Exemple
RC circuit :
Assuming zero initial Conditions :
where;
The D.C gain : K = 1
And Time constant T = R.C.

## Slide 12: D.C gain :
D.C Gain K of the system is ratio between the input signal and the output signal at the steady state. (i.e. p = 0 or t = ∞)
Examples
1)
K=10 and T=3
In standard form:
=
=
=
K=3/5 and T=1/5
2)

## Slide 13
Governing differential equation:
Laplacian of the response, Assuming zero initial Conditions :
s(t)=Kδ(t)
S(p)=K
S(p)=
Time-domain response:
Applying Inverse Laplace Transform
s(t)
e(t)
s(t)=
he D.C gain
time constant.
Impulse response of an linear time invariat (LTI) system
The impulse response of a system is The response of the system when the input is an impulse signal. It is represented as h(t).
The impulse response is a characteristic of an LTI system.
The output of a system to any input is calculated by convolving the input with the impulse response of the system
impulse Response

## Slide 14
y(t)=
Impulse response of an linear time invariat (LTI) system

## Slide 15
Step Response of First Order System
It is the response of the system when the input is the step signal.
Consider the unit step signal as an input to first order system, so Eo: e(t) = Eo u(t).
Laplace transform: E(p)=E0/p.
The reponse is :
DO partial fractions of S(p):
s(t)
e(t)
Step Response
S(p)=
Apply inverse Laplace transform, we obtain:
s(t) = KE0(1 − e −t/T )
The following figure shows the unit step response
The value of the unit step response, s(t) is zero at t = 0. It is gradually increasing from zero value and finally reaches to one in steady state. So, the steady state value depends on the magnitude of the input.

## Slide 16
Step Response of First Order System
Time constant T of a system is defined as the time required by the system to achieve 63.2 percent of the final value. =1/real part of pole location
s(t) = 3(1 − e −t/2 )
When t = T:
s(t) = K(1−e −1 ) = 0.632K

## Slide 17
(1) Changing D.C. gain:
(2) Changing Time constant:

## Slide 19
Example: same RC circuit: R = 1KΩ et C = 10µF ( with time constante T = R.C = 0.01s) and unit step with amplitude Eo = 1 V . The reponse is represented by the following figure:

## Slide 20: Ramp Response :
With slope a : e(t) = a.t
E(p) = a /
Laplace transform, I C=0:
  Ramp response is the response of the system when the input is the Ramp signal.
s(t)
e(t)
Ramp Response
The reponse is :
DO partial fractions of S(p):
S(p)=
Apply inverse Laplace transform, we obtain:
s(t) = Ka( t - T + e −t/T )
The figure is the unit ramp response
Example: K = 1 and T = 1: y(t) = t − 1 + e −t
If T increases, Error will increase.

## Slide 21
Exemple : Circuit RC with : R = 1KΩ et C = 10µF (T = R.C = 0.01s) and ramp with slope a = 1 V/S.

## Slide 23
Second-order system:
Consider the following block diagram of closed loop control system. Here, an open loop transfer function, / p(p+2δ) is connected with a unity negative feedback.
s(t)
e(t)
+
-
H(p)==
=
H(p)= ==
Hence, the above transfer function is of the second order and the system is said to be the second order system

## Slide 24
Second-order system:
If the power of ‘p’ is two, the system is said to be the second order system :
Applying Laplace transform and assuming zero initial Conditions :
A Governing differential equation is given by
+ Ke(t)
,τ and K>0
Where k is DC gain, τ is damping ratio (without unit) and is undamped natural frequency
+ p KE(p)
H(p)==

## Slide 25
The transfert fonction :
Le discriminent réduit s’´écrit : est souvent utilisé lorsque le coefficient
b est pair (b=2b’).
If ξ ≥ 1 over damped
> 0
Real roots
The two roots are complex conjugate when 0 < δ < 1.
The characteristic equation is:
The roots of characteristic equation are:
= 0 pôle double
< 0

## Slide 26
According to the value of ζ, a second-order system can be set into one of the four categories:
S1,2 =±
Where, Damped natural frequency
S1,2 =-

## Slide 27
EXAMPLE : RLC circuit

## Slide 28: Step REPONSE :
Step input with amplitude Eo : e(t) = Eo.
Applying the Laplace transfor :
Step reponse over damped
The response is:
ζ > 1

## Slide 29
Time domain response:
Step reponse with : K = 1 ; z = 1,5 et ωn = 10rad/s
Seems the first order system.
Tends toward K.Eo in the infinite time.

## Slide 30: réponse indicielle en régime critique (z = 1)
La réponse est de la forme :
Après transformation inverse, il vient :
réponse indicielle d'un système du second ordre avec : K = 1 ; z = 1 et ωn = 10rad/s
La valeur de la réponse en régime permanent est KEo.
On remarque que le système est plus rapide que dans le cas précédent.

## Slide 31: Step reponse under damped
The reponse :
The time reponse :
ζ < 1

## Slide 32
Step reponse for : K = 1 ; ζ = 0,2 et ωn = 10rad/s
For ζ < 0.7 the system is oscillating
The permanente reponse tends toward K.Eo

## Slide 33: Influence of z on the shape of the step response.
Step reponse with : K = 1 ; ωn = 10rad/s and various ζ = 0.2 0.5 0.7 1 6
ζ = 6: the system becomes excessively slow.
For ζ = 1, there is no overshoot (dépassement) or oscillation.For ζ = 0.7 the system is oscillatory, oscillation no longer being perceptible after half a period.At ζ = 0.5, the system oscillates over one period.
If damping is too low (ζ = 0.2), the system becomes excessively oscillatory.
If ζ increases the damping is increases to the response.
If ζ decreases the damping is decreased and the system begins to oscillate.
If ωn increases the oscillation frequency will increase.

## Slide 36: Le temps de réponse à 5%
La rapidité est définie par le temps de réponse du système soumis à une entrée en échelon d'amplitude Eo. En pratique, on mesure (ou on calcule) le temps que met la réponse à rester dans une zone comprise entre plus ou moins 5% de la valeur visée.
Temps de réponse à 5% d'un système non oscillant.
Pour un système oscillant, le temps de réponse n'est pas le temps au bout duquel la réponse atteint 95% de la valeur visée mais le temps au bout duquel la réponse reste définitivement dans la zone 0,95.Eo / 1,05.Eo. On peut immédiatement remarquer que plus le système va osciller, plus son temps de réponse va augmenter : Tr5% traduit le compromis rapidité/stabilité.
Temps de réponse à 5% d'un système oscillant.

## Slide 41: AMORTISSEMENT / STABILITÉ.
Un bon amortissement est la capacité d'un système oscillant à être suffisamment amorti et à ne pas présenter de dépassement important. Cela signifie deux choses :
* Le premier pic de la réponse ne devra pas dépasser de manière trop importante la valeur visée :
Le nombre d'oscillations avant stabilisation devra être faible.
D'un autre coté, on ne veut pas que le système soit excessivement amorti (Fig.4) car l'augmentation de l'amortissement provoque une diminution du rendement du système asservi. En effet, l'amortissement correspond physiquement à des pertes d'énergie : frottements en mécanique, courants de Foucault en électricité, pertes de charges en hydraulique, etc. Les performances sont alors diminuées.
Le critère de "bon amortissement" correspond à des réponses du type de celles représentées Fig.2 et Fig.3.
Qualitativement, on peut distinguer quatre cas d'amortissement

## Slide 42
Réponse insuffisamment amortie.
Conséquences:
Dépassement D1 trop important.
Temps de réponse trop grand.
Oscillations mécaniques dangereuses.
Réponse correctement amortie.
C'est le meilleur cas de figure :
Dépassement D1 faible.
Temps de réponse petit.
Pas d'oscillations.
Well-damped response with no overshoot.
In such situations, the damping value is slightly higher than in the previous case. La valeur de l'amortissement est alors un peu plus importante que dans le cas précédent.
Consequences:
Zero overshoot (D1).
Response time is slightly longer but still acceptable.
No oscillations.
Overdamped Response.
Consequences:
Zero overshoot (D1).
High response time: slow system.
No oscillations.
Underdamped Response.
Consequences:
Excessive overshoot (D1).
Excessive response time.
Potentially dangerous mechanical oscillations.
Correctly Damped Response.
This is the best-case scenario:
Low overshoot (D1).
Short response time.
No oscillations.

## Slide 44: Exercice 02

## Slide 46: Example 3