## Slide 1
control system and regularization
BE521 _ L3
Produced by:
Mme Iles Amel
بسم الله الرحمن الرحيم

## Slide 2: lecture 4
Frequency response analysis

## Slide 3: Introduction :
Frequency response is the steady state response of a system to a sinusoidal input.
In frequency response method, the Frequency of the input signal is varied over a certain range and the resulting response is studied.
Lets a system with transfer function H(p), subjected to a harmonic input of amplitude Eo :
e(t) = E0 sin ωt .
We can fully describe an LTI system by looking at how it changes the gain and phase of every single frequency across the spectrum.
LTI
system
Output sin
s(t)
Input sin
e(t)
Same frequency
s(t)= S0.sin (ωt +phase)

## Slide 4
H(jω) is therefore a complex number with magnitude S0/E0 and argument φ.
H(jω) is called the system's frequency response and characterizes it completely.
There's no longer any need to solve the system's input/output differential equation to know its response to a harmonic input.
Using transfer plot, we can predict the stability of closed-loop systems from their open-loop transfer functions.
These plots enable stability measurements to be carried out and gain and phase margins to be defined, representing the safety margins of a control system.
We use the semi-logarithmic scale to plot gain and phase curves.
A semi-logarithmic plot/graph has one axis on a logarithmic scale, the other on a linear scale

## Slide 5: Recall: Polar form of complex numbers
=r=,
Arg(Z)= ∟Z== arctan()

## Slide 6
Bode plots
The Bode plot or the Bode diagram consists of two plots :
Magnitude plot in dB
Phase plot
– In both the plots, x-axis represents angular frequency (logarithmic scale). Whereas, yaxis represents the magnitude (linear scale) of open loop transfer function in the magnitude plot and the phase angle (linear scale) of the open loop transfer function in the phase plot.
The magnitude of the open loop transfer function in dB is
Adb(ω) = 20 function of Log10 (ω)
where is the amplitude or gain
• A decade is defined as any 10-to-1 frequency range
• An octave is any 2-to-1 frequency range.
The "magnitude" of H is simply the complex absolute value:
– The phase angle of the open loop transfer function in degrees is
φ : Phase = Argument.
Unity gain:1 we have 1=0db

## Slide 7: Example 1: Constant
Draw the bode plot of the transfert fonction of T( p)=k.
Solution:
Let's put p = j ω
T(p)=k
;
tg =

## Slide 8
Basic frequency response factors

## Slide 9
The following table shows the slope, magnitude and the phase angle values of the terms present in the open loop transfer function. This data is useful while drawing the Bode plots.

## Slide 10
Example 2: Zero at origin
Consider the open loop transfer function G(p)H(p)=p
Magnitude M=20logω dB
Phase angle ϕ=90°
At ω=0.1rad/sec, the magnitude is -20 dB.
At ω=1rad/sec, the magnitude is 0 dB.
At ω=10 rad/sec, the magnitude is 20 dB.
The magnitude plot is a line, which is having a slope of 20 dB/dec. This line started at ω=0.1rad/sec having a magnitude of -20 dB and it continues on the same slope. It is touching 0 dB line at ω=1 rad/sec.
In this case, the phase plot is 900 line.

## Slide 11
Example 3: Simple zero
Consider the open loop transfer function T(p)=1+pT.
Magnitude M(db)=20 log dB
Phase angle = degrees
For w < , the magnitude is 0 dB and phase angle is 0 degrees.
For w > , the magnitude is 20logωτ dB and phase angle is 90°.
The magnitude plot is having magnitude of 0 dB up to ω=1/τ rad/sec. From ω=1/τ rad/sec, it is having a slope of 20 dB/dec. In this case, the phase plot is having phase angle of 0 degrees up to ω=1/τ rad/sec and from here, it is having phase angle of 900. This Bode plot is called the asymptotic Bode plot.

## Slide 12: Example 4: Simple pole
The magnitude plot
The transfert function T(p) of the first order system : T(jw)=
M(dB)=
M(dB)=

## Slide 13
If ω tends toward 0 :
M(dB)=logk= Constante
If ω tends toward infinity : M(dB)=logk-20 log - 20 log w= 20 log - 20 logw
= Constante + a slope of (-20 dB/dec)
The intersection of the two lines occurs at a point of frequency ωo such that :
The corresponding pulsation is =; It is called the breaking pulsation.
Bode magnitude plot

## Slide 14
The real curve is situated at -3dB: -3 dB correction at the corner frequency
In the same way, we find :
For w== ; =
M(dB)=
Bode magnitude plot

## Slide 15
* for low frequencies: 20logK line
* for frequencies around 1/ : points indicated at -1, -3 and -7 dB.
* for higher frequencies: slope -20dB/decade.
For a first-order system, the breaking pulsation is equal to 1/
Bode magnitude plot

## Slide 16
Recall:
Phase angle is given by:
For ω = 0 : φ(ω) = Arctg(0) = 0
For ω tends toward infinity : (w)=arctg(--=-90°
Bode phase plot

## Slide 17
The asymptotic diagram has the shape of a staircase step with a phase shift jump at the breakpoint:

## Slide 18: Example 1
RC circuit with :
R = 1KΩ et C = 10µF
Time constant T = R.C = 0.01s.
It is a unity-gain system with transfer function :
T(p)=
The low-frequency gain is :
AdB = 20logK = 20log1 = 0dB.
The cutoff frequency or corner frequency :
ωo = 1/T = 1/0.01 = 100 rad/s.

## Slide 19: identification System
Our system is modeled by the transfer function :T(p)=
To generate a bode, Nyquist or Nichol plot, we could solve the transfer function mathematically and draw the curves using the equations that we come up with.
However, this method assumes that we already have the transfer function to start with.
So let’s assume that we don’t have this model. We’re working with hardware directly like a physical electrical circuit.
We know that this can be modeled as an LTI system, but we don’t yet have a model. This is just a black box to us where we can apply different inputs and measure the outputs.
LTI: black box
Output sin
s(t)
Input sin
e(t)
hardware

## Slide 20: RC circuit example : R = 1KΩ et C = 10µF
First measure: We could apply a voltage as a sine wave at 10 radian per second and with a known amplitude: : e1(t) = Eo sin(ω.t) = sin(10.t), and compare it to the measured output voltage once all of the initial transients die down. And by overlaying these two, we could calculate the resulting gain or change in amplitude and the resulting phase shift.
The output signal differs very little from the input signal. There is a slight delay R1 = 1ms, but the amplitude difference is not measurable. We calculate the amplitude ratio in decibels and phase :
Magnitude in db:
AdB = 20logA1 = 20 log (1) = 0 dB
Phase is calculated by
φ = -R1.ω = - 0,001.10 = - 0,099 rad = -5,71°.

## Slide 21
Let’s get another one : we will feed though an input voltage with a frequency of 100 rd/sec: e2(t) = Eo sin(ω.t) = sin(100.t) and check this out.
At this slower frequency, The output signal is already weaker (magnitude A2 < Ao) and delayed (delay R2) :
Measures give:
Magnitude E2 = 0.7 Volts with delay R2 = 7,8 ms.
The amplitude ratio in decibels :
AdB = 20logA = 20 log (0,7) = - 3,09dB
The phase is:
φ = - R2.ω = - 0,0078.100 = - 0,78 rad = -45°.

## Slide 22
Third measure : : we will feed though an input voltage with the same amplitude and a frequency of 200 rd/s: e3(t) = Eo sin(ω.t) = sin(200.t).
The output signal is further attenuated (amplitude A3 < A2 < Ao) and delayed (delay R3): measurements give: amplitude E3 = 0.44 Volts and delay R3 = 5.5 ms.
Amplitude in decibels is calculated: AdB = 20logA = 20 log (0.44) = - 7.1dB
and the phase shift:
φ = - R3.ω = - 0.0055.200 = - 1.1 rad = -63°.

## Slide 23
Forth measure : : Another measure at the faster 1000 rd/s: e4(t) = Eo sin(ω.t) = sin(1000.t) :
The output signal is very weak (amplitude A4 < A3 < A2 < Ao) and very delayed (delay R4): measurements give:
Amplitude E4 = 0.1 Volts and delay R4 = 1.5 ms.
We calculate the amplitude ratio in decibels:
AdB = 20logA = 20 log (0.1) = - 20dB
and the phase shift
φ = - R4.ω = -0.0015.1000 = - 1.5 rad = -84.28°.

## Slide 24: Let's group the results in a table:

## Slide 25: Let's take the bode diagram of the RC circuit under consideration:
For pulsation ω = 10rad/s (low frequency), we read:
AdB = 0 dB and φ = -5°.
For pulsation ω = 100rad/s (the breaking pulsation), we read AdB = -3 dB and φ = -45°.
For pulsation ω = 200rad/s, we read AdB = - 7dB and φ = - 63°.
For pulsation ω = 1000rad/s (high frequency), we read AdB = - 20dB and φ = - 85°.
The bode diagram clearly shows the experimentally measured results.

## Slide 26
The cut-off frequency of a system is often considered to be the frequency at which the output signal loses three decibels (corresponding to a 30% decrease),
Remember, we don’t have the model of this system. We got this information by measuring the behavior of the physical circuit. But from this information, we can fit a model to this result.
For example, we can see that this system has a low pass filter like behavior since the low frequency signals are passed nearly unaltered and the high frequency signals are attenuated. We can also tell that there are one pole since the magnetude at higher frequencies slope down at negative 20 db/dec. And we can also see that there is a slightly damped mode around 100 rd/sec. And by looking at this bode plot, we could fit a transfer function or a model to this data that approximates this response.
A first-order system is a low-pass filter up to its cutoff frequency.

## Slide 27: Example 5: 2nd order System Response
Denominator in a + jb form, we obtain :
Magnitude :
Assuming :
T(p)=
T(jw)=

## Slide 28
When ω tends toward 0, u tends towards 0 et :
M(dB) = 20logK =Cte Recall: log(1) = 0
M(dB) tends towards a horizontal line.
When ω tends to infinity, u tends to infinity
M(dB) = 20logK - 20 log)
M(dB) = 20logK +a slope of (-40 dB/dec)
The two lines intersect at a point such that :
The corresponding pulsation is ω :
Bode magnitude plot

## Slide 29
* for low frequencies: straight line 20logK
* for frequencies around ωn: magnitude value depends on z (resonance or not).
* for higher frequencies: slope -40dB/decade.
Bode magnitude plot

## Slide 30
When ω = 0 : φ(ω) = Arctg(0) = 0
When ω tends toward infinity : (w)=-arctg()=-
Around ω = ωn : ()=-arctg(--
Bode phase plot

## Slide 31
With nonminimum phase or unstable plants, bode plot can be misleading. And so this is where a Nyquist plot is useful.
The asymptotic diagram has the shape of a staircase step with a phase shift jump at the undamped natural pulsation:
Bode phase plot

## Slide 32
BLACK-NICHOLS plot
NICHOLS is a single graph like Nyquist, but it plots the information on a Cartesian grid. Magnitude A(ω) of H( jω) is the vertical axix in dB (Adb(ω) = 20 ), and phase φ(ω) is the horizontal axis in degrees. So it’s the exact same units as the bode plot.
In fact, it is the Bode plot information, just packaged onto a single chart. And it’s easier to visualize if we align the magnetude and phase plots with the nichols chart. And as we trace through the frequencies, we can see how the bode plot information is mapped into this single graph.
The black diagram is the representation in the (ω,φ) plane of H(jω).
The curve can be plotted point by point using the particular values found previously, namely :
1st order system :
M(dB)=
(w)=arctg(w)

## Slide 33
we find features identical to those of the bode diagram:
with increasing frequency: the phase shift varies between 0 and π/2 and gain varies between 20 logK and 0dB.
This curve is graduated in pulses, with the arrow indicating their increasing direction.
BLACK-NICHOLS plot

## Slide 34: Example 1 : RC circuit with : R = 1KΩ et C = 10µF and time constante T = R.C = 0.01s.
We find a low-frequency gain:
AdB = 20logK = 20log1 = 0dB.
Cut off pulsation
ωo = 1/T = 1/0.01 = 100 rad/s.
vertical phase φ = -45°.
T(p)=

## Slide 35: 2eme ordre System:
We know that :
Remarkable values are :
As with the Bode diagram, there are as many responses as there are values of the damping factor .
T(jw)=

## Slide 36: Example :
Transfer function systems
T(p)=
For = 0.03; 0.1; 0.2; 0.4; 0.7; 1

## Slide 37
NYQUIST plot:
A NYQUIST plot still displays gain ‘A(ω) ’, phase, and frequency ‘φ(ω) = Arg [H (jω)] ’, it does so all on a single chart and with polar coordinates. Gain is the radial component or the distance from the origin on a linear scale. So we’re not dealing with decibels here.
And phase is the angular component or distancearound the origin.
And frequency isn’t shown directly, but as we progress along this curve, the frequency is changing.
For a pulsation of 10rad/s, we read the amplitude A(10) by measuring the segment OM and thethe phase shift φ(10) by measuring the polar angle φ: this is a representation inpolar coordinates. The arrow on the plot indicates the increasing direction of pulsations point O is reached when ω = ∞. The phase shift is generally negative.

## Slide 38: Polar plot of First-Order term:
Assuming that the first-order term is in numerator: T(p)=p+1
T(jw)=1+jw
the NYQUIST plot use a upper half : it is a mirror image of the lower half, and it shows the response for negative frequencies, which are typically not shown on the bode plot.
Also notice the critical point, the one we’re trying to avoid for oscillations. It’s just a single point on a Nyquist plot, and it corresponds to negative 180°and a gain of 1.

## Slide 39
Assuming that the first-order term is in denominator:
T(p)= T(jw)=

## Slide 40
The polar plot of this transfer function is a semicircle as the frequency ω is varied from zero to infinity, as shown in Fig. The center is located at 0.5 on the real axis, and the radius is equal to 0.5.

## Slide 41
This curve should be graduated in pulses, with the arrow indicating increasing direction.
At very low frequencies, the phase shift is zero and the amplitude is K. The breaking pulse ωo = 1/T: this corresponds to the point with abscissa K/2 and ordinate K/2 (the point where the semicircle turns back). At this point, phase (polar angle) = - π/4.
At high frequencies, gain tends towards 0: point (0,0) on the diagram (this point is never reached, as it corresponds to an infinite pulsation). Phase tends towards -π/2
ATTENTION: gain is not expressed in decibels
In general,

## Slide 42
Example 1 : RC quadripole with : R = 1KΩ and C = 10µF with time constant T = R.C = 0.01s.Low-frequency gain K = 1: point (1,0) on diagram.
Breakpoint pulse ωo = 1/ = 1/0.01 = 100 rad/s. It corresponds to the point with abscissa 1/2. At high frequencies, the gain tends towards 0: point (0,0) on the diagram.
NYQUIST plot of RC circuit with H(p)=

## Slide 43: Polar plot of Second-Order term:
When w tends toward 0: M(dB)=1 and 0°
When w tends toward : M(dB)=0 and )180°
The polar plot of underdamped, second-order transfer function starts at 1∟0 and ends at 0 ∟-180 as ω increases from zero to infinity. Thus, the high-frequency portion of G(jω) is tangent to the negative real axis as shown in Fig.
remarkable points :
for ω = 0, T(jω) = K pure real (r = K and φ = 0): At very low frequency, the phase shift is zero and the amplitude is K.
for ω = ωn, T(jω) = K/2zj = -jK/2z pure imaginary (φ = -90°): The breaking pulse ωn is located at the intersection of the response curve with the imaginary axis.
for ω = ωr, (case where z < 0.7), we obtain the maximum modulus, i.e. the highest value of OM.
for ω tending towards infinity, H(jω) tends towards zero with negative values: at high frequencies, gain tends towards 0: point (0,0) on the diagram (this point is never reached since it corresponds to an infinite pulsation). Phase tends towards -π
T(jw)=

## Slide 44: Example :
Transfer function systems
T(p)=
for z = 0.03; 0.4; 0.5; 0.7; 1; 5.
A second-order system is a low-pass filter.

## Slide 45: Rules for Drawing Nyquist Plots
Locate the poles and zeros of open loop transfer function G(s)H(s) in ‘s’ plane.
Draw the polar plot by varying ω from zero to infinity. If pole or zero present at s = 0, then varying ω from 0+ to infinity for drawing polar plot.
Draw the mirror image of above polar plot for values of ω ranging from −∞ to zero (0− if any pole or zero present at s=0).
The number of infinite radius half circles will be equal to the number of poles or zeros at origin. The infinite radius half circle will start at the point where the mirror image of the polar plot ends. And this infinite radius half circle will end at the point where the polar plot starts.
Stability Analysis using Nyquist Plots

## Slide 46: Nyquist Criterion
Because the Nyquist criterion is a graphical method, we need to establish the concepts of encircled and enclosed, which are used for the interpretation of the Nyquist plots for stability.
Encircled: A point is said to be encircled by a closed path if it is found inside the path. For example, point A in Fig. 5(a) is encircled by the closed path Γ, because A is inside the closed path. Point B is not encircled by the closed path Γ, because it is located outside the path. Enclosed: A point is said to be enclosed by a closed path if it lies to the left of the path when the path is traversed in CCW direction. The concept of enclosure is particularly useful if only a portion of the closed path is shown. For example, point A in Fig. 5(b) is enclosed by Γ. However, point B isn’t enclosed

## Slide 47
Number of Encirclements (N) When a point is encircled by a closed path Γ, a number N can be assigned to the number of times it is encircled. The magnitude of N can be determined by drawing an arrow from the point to any arbitrary point s1 and consider it as starting point, then follow the path in the prescribed direction until it returns to the starting point. The total net number of revolutions is N, which is positive for CCW encirclement and negative for CW encirclement. For example, point A in Fig. 6(a) is encircled once in CW direction (N= - 1) and point B is encircled twice in CW direction (N= - 2). In Fig. 6(b), point A is encircled once in CCW direction (N=+1), and point B is encircled twice (N=+2).

## Slide 48
The stability of linear control systems is analysed by constructing the Nyquist path, which is a closed contour in the s plane enclose the entire right-half of s plane. The contour consists of the entire jω axis from ω=–∞ to ∞ and a semi-circular path of infinite radius in the right-half of s plane in the clockwise (CW) or counter clockwise (CCW) direction. Therefore, the Nyquist path encloses the entire right-half s plane and encloses all the zeros and poles of 1+G(s)H(s) that have positive real parts as shown in Fig. 7 (a). The Nyquist path must not pass through poles or zeros of G(s)H(s), if the function G(s)H(s) has poles or zeros at the origin (or at any point on the jω axis), the Nyquist path must be modified by using a semicircle with radius ε → 0 as shown in Fig. 7 (b).