## Slide 1
control system and regularization
BE521 _ L3
Produced by:
Mme Iles Amel
بسم الله الرحمن الرحيم

## Slide 2: lecture 5
Stability Analysis

## Slide 3: Introduction
The Stability of a linear closed loop system can be determined from the locations of closed loop poles in the p-plane.
General stability condition
The analysis of, whether the given system can reach steady state; passing through the transients successfully is called Stability Analysis of the system.
Stability condition based on the location of the closed loop poles
For example, a process transfer function G(s) represented as
G(p)=
Two poles: =-1 and =-2
One Zero: Z=-0.5

## Slide 5: Introduction
Algebraic stability criterion.
The closed loop poles are roots of the characteristic equation.
if the characteristic equation is of higher order, then it is not possible to calculate it’s roots to determine the closed loop poles.
characteristic equation: D(p)=Bnpn+Bn-1pn-1+ ... B1p+B0=0
Necessary conditions of stability :
all the coefficients of the polynomial must have the same sign.
None of the coefficients vanishes, ie; all the powers of ‘p’ must be present in the characteristic equation.
These two conditions are necessary for a system to be stable, but not sufficient:If any polynomial satisfies the above 2 conditions, it is called as Hurwitz polynomial.

## Slide 6
Routh- Hurwitz criterion.
R-H Criteria is a mathematical test that is necessary and sufficient condition for the stability of an LTI system.
 Method of forming Routh’s Array :
The first two rows can be directly written from the characteristic equation.
Third row :
calculate coefficients C, D, E …etc.
Fourth row : same calcul
….and so on until the last line
Routh’s stability criterion.
All the terms in the first column of the Routh’s array must have the same sign.
There should not be any sign change in the first column of Routh’s array.

## Slide 7: Example 1
G(p)=
Consider the polynomial D(p ) = + 6+11p+6 to construct the Routh table.
No of sign changes : the number of poles in right half plane 0. the system will be stable.
We can check that D(p ) = + 6+11p+6 =(p+3)(p+2)(p+1) whose roots are real and all negative : -3, -2 and -1

## Slide 8
Oscillations (stabilité marginale).
If all the coefficients in any derived row are zero, it indicates that there are roots of equal magnitude lying radially opposite in the p plane, that is, two real roots with equal magnitudes and opposite signs and/or two conjugate imaginary roots.
In such a case, the evaluation of the rest of the array can be continued by forming an auxiliary polynomial with the coefficients of the last row and by using the coefficients of the derivative of this auxiliary polynomial in the next row. Such roots can be found by solving the auxiliary polynomial, which is always even.

## Slide 9: Exemple 2 : special case
Consider the polynomial D(p ) = + +6p+4 to construct the Routh table.
Row of zero ‘RoZ’: effect: the term of next row can not be determined and the Routh test fails.
From a polynomial by using the coefficients of a row which is just above the RoZ.
Such a polynomial is called Auxiliary Polynomial A(p):
Take the derivative of auxiliary polynomial : 0
Replace the RoZ by the coefficients of
Case 1: First element of any of the row’s of Routh’s array is Zero and the remaining row contain criterion.
Case 2: All the elements of a row in a Routh’s array are zero.
G(p)=

## Slide 10
We can check that:
D(p ) = + +6p+4=(+2)(p+1)(p+2)=(p+j) (p-j)(p+1)(p+2)
the previous line : 2
Or :
derived polynomial : 2p
Replacement line: 2 0
the terms in the pivot column are all positive and the system is stable
It has two pure imaginary conjugate complexes roots and two negative real roots -1 and -2.

## Slide 11
Avantages:
This criterion is used to discuss the stability of a system as a function of the variation in its parameters.
Disadvantages :
Calculations quickly become complex as soon as the order of the transfer function increases.
The transfer function of the system must be explicitly known.
This criterion does not allow adjustment (theoretical absolute stability).
IN CONCLUSION ON THE ROUTH CRITERION :

## Slide 12
Stability margins measure how close a closed-loop system is to instability, that is, how large or small a change in the system is required to make it become unstable. The two commonly used measures of stability are the gain margin and the phase margin.
The gain margin is the amount of allowable variation in the gain of the plant before the closed-loop becomes unstable.
As a rule of thumb, the closed-loop should remain stable for gain variations in the range [0.5, 2] (= ±6dB).
The phase margin is the amount of allowable variation in the phase of the plant before the closed-loop becomes unstable.
As a rule of thumb, the closed-loop should remain stable for phase variations in the range ±45°
Stability Margins

## Slide 13
A system is stable if the gain and phase margins are both positive
Gain margin:
the difference (in dB) between 0dB and the system gain, computed at the frequency where the phase is 180°
Phase margin:
the difference (in °) between the system phase and 180°, computed at the frequency where the gain is 1 (i.e., 0dB)

## Slide 14: . Critères graphiques.
Critère simplifié de stabilité : Une commande linéaire en boucle fermée est stable si le gain de la FTBO est inférieur à 1 (0dB) lorsque la phase vaut -180°. On définit la pulsation critique ωo telle que φ(ωo) = −180°. La condition de stabilité s'écrit alors : A(ωo) ≤ 1.
Marge de gain :
Marge de gain de 6dB
On définit alors la marge de gain comme étant la valeur du gain, prise en valeur absolue, pour la pulsation critique.
La figure montre un exemple de réglage du gain avec une marge de 6dB sur un diagramme de Bode. La FTBO de gain statique Alim est à la limite de l'instabilité. En translatant de 6dB vers le bas cette FTBO sur le diagramme de gain, on obtient une nouvelle valeur du gain statique Ao < Alim. Ao = Alim - 6dB. Le système sera réglé de telle manière que son gain statique en boucle ouverte soit égal à AodB.
Remarque: la translation de la FTBO sur le diagramme de gain n'affecte pas la courbe de phase car le déphasage dépend uniquement de la pulsation.

## Slide 15
On peut également définir une marge de phase qui, éloigne la courbe du point critique.
La marge de phase est la différence entre 180° et la valeur du déphasage pour la pulsation critique.
La figure montre un exemple de réglage avec marge de phase de 45°.
Marge de phase :
Marge de phase de 45°.
Les valeurs usuelles des marges de stabilité permettant un réglage correct des boucles d’asservissement sont :
Marge de Gain : 6dB à 15dB Marge de Phase : 40° à 45°

## Slide 16
On the Nyquist locus, the smaller the length L of the OA segment, the greater the gain margin, which is inversely proportional to this length. It is expressed in dB.

## Slide 17: The degree of stability is assessed by two stability margins:
The phase margin
MP=180°+Arg(T()
When the open-loop transfer function is explicitly known, it is possible to determine the stability margins algebraically. Otherwise, we use the experimental plot.
The gain margin
MG=-20 log
Arg(T()=-180°

## Slide 18
Solution:
a) Study stability as a function of k.
The closed-loop transfer function is : T(p) =
Example:
Consider a control system whose open-loop transfer function is given by : T(p) =
k > 0
We propose :
study stability as a function of k;
determine k for a gain margin of 6 dB and deduce the phase margin.
c) determine k for a phase margin of 45° and deduce the gain margin.
Routh's algebraic criterion.
The characteristic equation is given by : D(p) = p3 + 1.5p2 + 0.5p + k = 0.

## Slide 19
The associated Routh table is :
P3 1 0.5
P2 1.5 k
P1 0.75 - k 0<==line multiplied by 1.5 (depending on choice, we can multiply and divide by the same value) P0 k 0
Closed-loop stable system if: 0 < k < 0.75.
Note:
For k = 0.75, p1 contains a zero in the pivot column, so the associated auxiliary equation is 1.5 p2 + 0.75 = 0 and has the following solutions p = ± jwc = ± j0.707.
In this case, the closed-loop system is just oscillating with pulsation wc.
The controlled system is at the stability limit if and Arg(T()=-180°
Note that in this case: w1 = wc.

## Slide 20
Arg(G(jACw)) = - 180° è - 90° - Arctg(w) - Arctg(w/0.5 ) = - 180°.
Appliying the rool: Arctg(x ) + Arctg(y ) = Arctg[(x + y)/(1-xy)], we have :
è Arctg(3w / (1 -2w2)) = 90° è w = w1 = wc = 0.707
At the limit of stability, we have :
è k = 0.75.
Hence the same result, i.e. the closed-loop system is just oscillating with pulsation w1 = wc for k = 0.75.

## Slide 21
b) MG = -20log = 6 dB and wc = 0.707 (Arg(GH) = -180°)
è = 10-0.3
è k = 0.375
Note: From this result, we retain the practical formula MG = -20 log [k/kc]; where kc is the limit value of k below which stability is assured (here kc = 0.75) and k is the design value.
Phase margin :
MP =180° – 90° - Arctg(w1) - Arctg(w1/0.5 ), where w1 is such that :
; let’s :
We find: w1 = 0.485 and the phase margin: MP =180°-160° = 20°.

## Slide 22: c)
By definition, the phase margin is given by: MP =180° + Arg(GH(jw1),
We wish to have a phase margin: MP = 45°
Arg(GH(jw1)) = -135°
and w1 = 0.28
For this pulse, it is necessary that
Gain margin is easily deduced by the formula :
–20 log(k/kc) = -20 log(0.166/0.75) =13db

## Slide 23: Abaque de Black
Black's abacus graphically realizes the FTBO to FTBF transformation.
Let's consider a unitary feedback system :
The FTBO of this system is H(p). Its FTBF is : G(p)=
In the case of a unitary feedback system, the transition from FTBO to FTBF is therefore a transformation of the type : U→

## Slide 24
The Black chart graphically illustrates this transformation. For each point M of the FTBO plotted on this chart (point giving a gain and a phase shift for a given pulsation), we can read the corresponding gain and phase shift of the FTBF on the curve networks
Black.

## Slide 25
Example:
for point M with pulsation 0.6rad/s, we read :
16.5 dB and -93° in open loop H(p)
0dB and -8° on closed loop G(p).
OLTF(p)= on Aback plot