## Slide 1
Magnetique resonance imagering
Created by:
Iles Amel
بسم الله الرحمن الرحيم

## Slide 2: Chapitre 4
MRI image reconstruction

## Slide 3
Image reconstruction is a mathematical process performed by the computer. It transforms the data collected during the acquisition phase into an image. We can think of reconstruction as the process of sorting the signals collected during the acquisition and then delivering them to the appropriate image pixels. The mathematical process used is known as Fourier transformation.
The MR image formation process subdivides a section of the patient’s body into a set of slices and then each slice is cut into rows and columns to form a matrix of individual tissue voxels.
introduction

## Slide 4: Image reconstruction
The signals in MR imaging arise from multiple voxels, often from an entire slice recorded all at once. These voxels contain different materials with different spin densities and relaxation times. Furthermore, the main magnetic field (Bo) has often been purposely distorted by the use of gradients to change the frequency and phase of protons as a function of spatial position. The resulting total MR signal is thus the sum of thousands of FIDs and echoes arising from individual voxels with different amplitudes, frequencies, and phases.

## Slide 5: Image reconstruction
Sorting out this huge array of overlapping and interfering signals might seem impossible, but a number of very clever techniques have been developed to do just that. Such methods include frequency-encoding and phase-encoding.
Fourier transform methods also allow the data to be sorted out according to differences in frequency and accumulated phase.
A typical MR scan may contain over 4 million voxels, each generating its own tiny MR signal. With such a huge array to analyze, how does the scanner possibly sort out where each signal is coming from?

## Slide 6: Spatial Encoding
Spatial encoding is the process by which MRI acquires information about the location of protons (typically hydrogen nuclei) within the body to create a spatial map or image.
There are three different types of spatial encoding: slice selective excitation, frequency encoding, and phase encoding.

## Slide 7
Slice Selection
The first gradient action (Gz) in a cycle defines the location and thickness of the tissue slice to be imaged. We will illustrate the procedure for a conventional transaxial slice orientation. Other orientations, such as sagittal, coronal, and angled combinations, are created by interchanging and combining gradient directions.

## Slide 8
Two steps are required to uniquely excite a slice in 2D MR imaging:
1. Slice-Selective RF Pulse: To select a particular slice, a slice-selective RF pulse is applied. This pulse is tuned to a specific frequency that corresponds to the desired slice thickness. The RF pulse is usually applied perpendicular to the direction of the main magnetic field (B0), which is typically aligned with the z-axis.
2. Slice-Selective Gradient: Along with the slice-selective RF pulse, a gradient magnetic field (Gz) is applied in the z-axis direction. This gradient field is superimposed on the main magnetic field, causing a variation in magnetic field strength along the z-axis. The gradient field varies linearly, with the highest field strength at one end of the desired slice and the lowest field strength at the other end.
The combination of steps (1) and (2) insures that only protons within the chosen slice are excited.
Slice Selection

## Slide 9
Each slice has a different center frequency determined by its position (z) along the slice-select gradient (Gss), given by
= γ(Bo + z•Gss) = + γ•z•Gss
where Bo is the main magnetic field strength and is its corresponding Larmor frequency.
Each slice has a finite width (Δz) and so it contains a range of frequencies (Δ) centered around . These quantities are related by the equation
Δυ = γ • Gss • Δz
In common practice Δυ is held constant (on the order of 1000-2000 Hz) and slice thickness Δz is varied by adjusting Gss. Stronger gradients produce thinner slices, and vice versa.
Slice Selection

## Slide 10
Frequency Encoding
The figure shows how frequency-encoding may be used to specify position within a slice. Here a frequency-encoding gradient (Gf) begins on the left of the image at position x=0 and increases linearly along the horizontal axis. If the main (static) magnetic field is Bo, then the effective field B(x) at any point (x) along the horizontal axis is given by
B(x) = Bo + x
From the Larmor equation (υ= γB), we can easily show that the resonant frequency υ(x) also varies linearly with position (x) along the frequency-encoding axis:
υ(x) = γB(x) = γBo + γx• = + (x)
where is the main field Larmor frequency and (x) is the frequency offset based on position along the gradient.
we are still not able to discriminate between pixels within a column (e.g. A vs B vs C) because their frequencies overlap. Spatial detection in this second dimension will require phase-encoding.

## Slide 11: Phase-encoding
At Step 0 (baseline, when no phase-encoding gradient is has been applied) the total signal from A&B together can be written: So(t) = A sin ωt + B sin ωt = (A+B) sin ωt.
In Step 1 we apply a phase encoding gradient to dephase spins along the vertical axis. After the gradient has been turned off, the signal from each pixel in the AB column now has a different phase shift, represented by the small clock face arrows.
However, by making two observations with A and B shifted by different phases. A and B are two pixels in the same vertical column resonating at the same encoded frequency (ω).
Φ(y)=ɣ.Gy.y.τy

## Slide 12: Phase-encoding
Let us ignore all the other pixels and just concentrate on A and B. Furthermore, for simplicity, let us assume that pixel A was in the zero position of the phase-encoding gradient and did not change phase, while pixel B was in a higher portion of the gradient and gained exactly 180° of phase relative to A. The signal emitted from pixel A is unchanged and equals A sin ωt. The signal from pixel B is now inverted and equals −B sin ωt. The total signal from A&B is now S1(t) = A sin ωt − B sin ωt = (A−B) sin ωt.
From this single measurement in Step 1, we still do not know the individual amplitudes A and B, only their difference (A−B). Using information from both Step 0 and Step 1 together, we are able to extract the unique signal contributions by simple algebra:
½ [So + S1] = ½ [(A+B) + (A−B)] = A
and ½ [So − S1] = ½ [(A+B) − (A−B)] = B

## Slide 13: Phase-encoding
In this simple experiment we again play out only two phase-encoding steps. In Step 0 the PE gradient is off and the signals from all pixels remain in phase. In Step 2 we assume the pixels in the second row (B, D, and F) all acquire a phase shift of 180° relative to row 1. After each phase-encoding step, a single aggregate MR signal is recorded reflecting contributions from each of the six pixels. Hence in this simple example with only two phase-encoding steps, exactly 2 MR signals are recorded from the slice.
We expand our previous example to a 6-pixel one, showing how Fourier transformation is used to sort out overlapping signal contributions in two dimensions. Below is a 2x3 array of pixels (A-F) at the center of a brain image with frequency- and phase-encoding directions as designated.

## Slide 14: Phase-encoding
The first of these signals is acquired when there is no phase shift between the two rows. Fourier transformation of this MR signal generates a spectrum revealing three frequencies (ω1, ω2, and ω3), whose amplitudes (A+B), (C+D), and (E+F) are the sum of the pixel values in each frequency column. At this stage we only know the sums of the pixel values for each frequency column; we do not know the individual values for any cell.
When we record the MR signal from the whole sample after Step 1 (where the second row has been phase-shifted by 180°, the Fourier spectrum has changed. Again three frequencies can be separated, but this time their magnitudes are (A−B), (C−D), and (E−F). We still are not able to assign unique pixel values with this single measurement, because now only the differences in pixel values for each frequency column are known. Because the Fourier Transform has sorted out frequencies into three columns, the corresponding phase change information can now be decoded. As in the 2-pixel example, and algebraic manipulation of the data for each frequency column using data from each phase-shift allows us to determine A, B, C, D, E, and F uniquely.
A real MR image may have hundreds of pixels in each dimension, and hence requires hundreds of phase-encoding steps to decode, but the basic principles are the same.

## Slide 15: 2D Fourier Transform
A real image is much more complex than the six-pixel example, but the general principles remain the same. Several minor differences are immediately apparent, however. In MR imaging we typically use at least 256 divisions along the frequency-encode axis, and thus the first FT spectrum will have 256+ frequency "bars" rather than 3.
The number of echo signals acquired equals the number of phase encode steps, which is usually 192 or 256 rather than 2.
The phase shifts between the rows are not simple multiples of 180°, but vary from echo to echo depending on the size of the phase-encoding step.
Because each echo has been acquired using a different set of inter-row phase shifts, the spectral amplitudes (heights of the bars) for each echo cannot simply be added or subtracted to compute individual pixel values as before. In order to sort out where each signal in a frequency column has originated, a second FT must be performed.

## Slide 17: 2D Fourier transforms
The MR imaging process consists of two major functions:
The first is the acquisition of RF signals from the patient’s body and the second is the mathematical reconstruction of an image from the acquired signals.
During the acquisition process the signals are collected, digitized, and stored in computer memory in a configuration known as k space. The k space is divided into lines of data that are filled one at a time. One of the general requirements is that the k space must be completely filled before the image reconstruction can be completed.

## Slide 18: 2D Fourier transforms
In 2DFT imaging, each row in k-space corresponds to the echo data obtained from a single application of the phase-encoding gradient. By convention, rows near the center of the k-space grid are defined to correspond to low-order phase-encode steps, whereas those rows near the top and bottom correspond to higher-order phase-encodings. Since echo amplitudes are larger at the low-order phase-encode steps (there is less gradient-induced dephasing), the values of k-space will be greater near the center of the grid.

## Slide 19
The Fourier transform is a mathematical technique that allows an MR signal to be decomposed into a sum of sine waves of different frequencies, phases, and amplitudes.
Fourier showed that any periodic signal s(t) can be written as a sum of sine waves with various amplitudies, frequencies and phases
Joseph Fourier
where ai are amplitudes, ϕi are phase shifts, and ω is the fundamental frequency. The higher order frequencies 2ω, 3ω, etc. are called harmonics.
Fourier transform

## Slide 21
Fourier transformation is the mathematical procedure connecting s(t) and S(ω). If s(t) is specified, S(ω) may be computed, and vice versa. The equations require some knowledge of complex numbers and calculus to make sense:
The common use in RF-pulse design is the sinc function:
whose Fourier transform is a uniform band of frequencies, such as those defining a single slice in conventional 2D MR imaging.

## Slide 22: What are 2D Fourier transforms?
The same idea can be extended into 2D:
The diagram to the right shows how a 2D brain image could be decomposed into planar waves of different amplitudes and frequencies. The sum of these many waves is used to build up a planar image.
A 2-dimensional image can be decomposed into a set of planar waves varying in phase, frequency, amplitude, and direction.
Unlike linear waves in one dimension, 2D planar waves may occur in any direction across the image (left-to-right, top-to-bottom, at 30°, 129°, etc.) Thus the Fourier summation must include all these angles and directions to represent the full image.

## Slide 23: K space
The cells of k-space are commonly displayed on rectangular grid with principal axes kx and ky. The kx and ky axes of k-space correspond to the horizontal (x-) and vertical (y-) axes of the image. The k-axes, however, represent spatial frequencies. Each k-space point contains spatial frequency and phase information about every pixel in the final image. Each pixel in the image maps to every point in k-space.

## Slide 24: K space

## Slide 25: K space
Points along the kx-axis represent frequency components along the x-direction of the image. Conversely, points along the ky-axis reflect frequency components along the y-direction of the image. The k-space image of a square block whose sides are aligned with the x- and y-axes would look like the top image (right).
If the block were rotated by 45º, the dominant spatial frequencies corresponding to the edges of the block would now be oriented at a 45º angle to the kx- and ky-axes. The relation between angle of the planar image waves and k-space location is shown below.

## Slide 26: K space
Real images will, have frequency components in all directions, resulting in a "galaxy"-like appearance of k-space. A bright "star" at a particular location in k-space implies that the spatial frequencies that point represents are making a positive contribution to final image.

## Slide 27: K space
The data to fill k-space is taken directly from the MR signal but can be acquired in any order. The dominant method for filling k-space over the last 30 years has been the line-by-line Cartesian method. Today spiral and radially oriented trajectories are becoming more popular.
In the Cartesian method each digitized echo completely fills a line of k-space. The echo signal is recorded in quadrature, so each k-space point contains real and imaginary components. The k-space values on the left side of each row are obtained early in the evolution of the echo, while those on the right side are obtained later. The center of the echo (and hence largest values) occur near the middle of each row of k-space.

## Slide 28: FOV and k-space

## Slide 29
Interface

## Slide 30
Interface permettant de choisir le protocole selon le type d’examen
Il choisit le protocole selon le type d’examen, s’il s’agit d’un examen cérébral il doit sélectionner le bouton ‘Head’, s’il s’agit d’un examen abdominal il doit sélectionner le bouton ‘Abdomen’…etc.

## Slide 31
Zoom de la liste de protocole pour les images cérébrales

## Slide 32
Séquences utilisées par l’appareil pendant un examen cérébral.

## Slide 33
Types d’antennes radiofréquences sélectionnées à partir de l’interface