## Slide 1
Magnetique resonance imagering
Created by:
Iles Amel

## Slide 2: Chapter 6
Image contrast

## Slide 3: introduction
The MR image displays certain physical characteristics of tissue.

## Slide 4: introduction
Imaging Protocol
Each imaging procedure is controlled by a protocol that has been entered into the computer.
Issues that must be considered in selecting, modifying, or developing a protocol for a specific clinical procedure include:
The imaging method to be used
The image types (PD, T1, T2, etc.)
Spatial characteristics (slice thickness, number, etc.)
Detail and visual noise requirements
Use of selective signal suppression techniques
Use of artifact reduction techniques

## Slide 5: T1-weighting
The repetition time (TR) between two successive RF pulses determines the T1-weighting, i.e., the level of recovery of the longitudinal magnetization in T1:
If the repetition time (TR) is long compared to T1 (TR = 4T1), the longitudinal magnetization returns to its equilibrium position at the end of each cycle (98% recovery), allowing enough time for all spins to return to their initial state.
If the repetition time is short compared to T1 (TR ≤ T1), the longitudinal magnetization does not have enough time to recover its initial position at the end of each cycle (recovery ≤ 63%).

## Slide 6
Let’s consider, for example, two tissues (C) and (L) with different T1 values. Tissue (L) has a longer T1 than tissue (C).

## Slide 7
For a short TR, since tissue (C) has a shorter T1 compared to tissue (L), it will recover more quickly than tissue (L).

## Slide 8: Exemple
The T1 of fat is short, the T1 of tissues is intermediate, and the T1 of water is long. The figure illustrates an example comparing the intensities of the three longitudinal magnetization vectors for the three cases: fat, tissue, and water. With a short TR, there is a strong contrast between the three cases.

## Slide 9: T2-weighting
First, a long TR must be applied to minimize T1-weighting.
The echo time (TE) corresponds to the time after which the decay of transverse magnetization in T2 can be measured.
The echo time (TE) determines T2-weighting, that is, the level of decay of transverse magnetization in T2.
Pour TE court

## Slide 10: For a long TE

## Slide 11
The figure illustrates an example comparing the intensities of the three transverse magnetization vectors for the three cases: fat, tissue, and water. With a long TE, we observe a strong contrast between the three cases.

## Slide 12
T2-weighted brain image acquired from a 1.5 T MRI scanner.

## Slide 13: Proton Density Weighting
To weight a sequence in proton density, you should choose:
A long TR to minimize T1 weighting.
A short TE to minimize T2 weighting.

## Slide 14
The figures summarize the different weightings:
A short TR and a short TE produce a T1-weighted image.
A long TR and a long TE produce a T2-weighted image.
A long TR and a short TE produce a proton density-weighted image, meaning it is minimally influenced by T1 and T2.
Pondération T1
Pondération densité de proton
Pondération T2
TE
TR