## Slide 1
Acoustic Equipment AH843

## Slide 3: Course Content
Chapter I: Characterization of Sounds and Noise
Chapter II: Sound Propagation in Free Field
Chapter III: Sound Propagation in Enclosed Spaces
Chapter IV: Acoustic Insulation

## Slide 4: Definition of Sound
Sound is an auditory sensation caused by disturbances in an elastic medium.
Generated by a vibrating system called a sound source.
Propagates as an acoustic wave.

## Slide 5: Sound Wave
• A sound wave is the propagation of a disturbance.
• Requires a material medium (air, water, solids).
• Transfers energy without transporting matter.

## Slide 7: SOUND CHARACTERISTICS
The mathematical curve of a wave allows us to describe the evolution of the disturbance in the propagation medium: it represents the variation of the physical quantity considered as a function of time.

## Slide 8
SOUND CHARACTERISTICS

## Slide 9
- Period (T)
- Frequency (f)
- Wavelength (λ)
- Amplitude (A)
- Phase
- Celerity (c)
- Spectrum
SOUND CHARACTERISTICS

## Slide 10
1. Période (T) : It is the time that elapses between two consecutive identical vibrational states.
SOUND CHARACTERISTICS

## Slide 11
2. Frequency (f)
It is the number of repetitions of the same vibrational state (period) per unit of time, its unit is the Hertz (Hz).
SOUND CHARACTERISTICS

## Slide 12
3. Wavelength (λ)
It is the smallest distance separating two points having the same vibrational state.
Its unit is the meter (m).
It is the distance traveled during a period.
SOUND CHARACTERISTICS

## Slide 13
𝑐é𝑙é𝑟𝑖𝑡é 𝑐
𝜆 =
𝐹𝑟é𝑞𝑢𝑒𝑛𝑐𝑒 f
SOUND CHARACTERISTICS

## Slide 14
4. Amplitude (A)
Maximum elongation of a point from its equilibrium position.
SOUND CHARACTERISTICS

## Slide 15
5. Phase
This refers to two sound waves whose maximum amplitude occurs at the same time
SOUND CHARACTERISTICS

## Slide 16
6. Celerity
It is the speed of propagation of the wave along its direction, and which depends on the characteristics of the medium (density, compressibility).
C = 340 m/s in air, 1450 m/s in water...
(Therefore, the denser the medium, the greater the speed).
SOUND CHARACTERISTICS

## Slide 17
7. Spectrum
La décomposition d’un son en une succession d’harmoniques constitue le spectre de ce son.
Les harmoniques sont issus de la décomposition d’un son
périodique en une succession de sons dont les fréquences sont toutes des multiples d’une
même
fréquence f appelée fondamental : f,2f, 3f, 4f,etc.
SOUND CHARACTERISTICS

## Slide 18
SOUND CHARACTERISTICS

## Slide 19: CARACTERISTIQUES DU SON 28
III.
7. Spectre
The spectrum is represented graphically by plotting the frequencies on the x-axis and the energy of the harmonics on the y-axis.

## Slide 20
Pure sounds
Complex sounds
TYPE OF SOUND

## Slide 21
- Pure sounds
Pure sounds: sinusoidal, single frequency (e.g. tuning fork).

## Slide 22
2. Complex sounds
SON MUSICAL
Composed of multiple, superimposed frequencies or harmonics

## Slide 23
Complex sounds
Musical sounds (harmonics)

## Slide 24
The sound does not have a characteristic frequency.
Noise is a sound considered undesirable.
Complex sounds
NOISE
These are non-periodic and non-sinusoidal sounds